## Slide 1: BSP v1.0 vs BSP v2.0 Performance & Operational Comparison
Kafka Platform Benchmark & Architecture Assessment
Containerised Confluent Kafka (KRaft) on OpenShift

## Slide 2: Executive Summary
Comparison between BSP v1.0 (VM-based Kafka) and BSP v2.0 (OpenShift + CFK + KRaft)
BSP v1.0 metrics sourced from real multi-day production traffic
BSP v2.0 metrics sourced from controlled OpenMessaging Benchmark (OMB) tests
Objective: assess throughput, replication, latency, and operational stability

## Slide 3: Platform Overview – BSP v1.0
Infrastructure: BVP v1.0 (Virtual Machines)
Kafka Deployment: Traditional VM-based Kafka
Metadata Management: ZooKeeper
Workload Type: Real production traffic
Operational History: Long-running, stable workloads

## Slide 4: Platform Overview – BSP v2.0
Infrastructure: BCP v2 (Red Hat OpenShift)
Kafka Deployment: Confluent for Kubernetes (CFK)
Metadata Management: KRaft (ZooKeeper-less Kafka)
Workload Type: Controlled OpenMessaging Benchmark (OMB)
Operational Model: Containerised, cloud-native

## Slide 5: Nature of the Data Compared
BSP v1.0 metrics represent real, sustained production workloads
BSP v2.0 metrics represent short-duration synthetic benchmark tests
Key interpretation guidance:
  BSP v1.0 shows proven long-term stability
  BSP v2.0 shows maximum capability and scalability potential

## Slide 6: Throughput Comparison – Ingress (Bytes In/sec)
BSP v1.0 (VM-based):
  Sustained ingestion: 40–90 MB/sec
  Peak ingestion: ~150 MB/sec
  Predictable daily traffic patterns
BSP v2.0 (OpenShift / CFK):
  OMB ingestion: ~50 MB/sec to >200 MB/sec
  Achieved despite shared BCP v2 infrastructure
  Short test duration and disk/resource constraints
Assessment:
  BSP v2.0 matches or exceeds BSP v1.0 peak ingestion
  No fundamental throughput ceiling introduced by OpenShift

## Slide 7: Throughput Comparison – Egress (Bytes Out/sec)
BSP v1.0:
  Sustained BytesOut: 200–500 MB/sec
  Peaks up to ~600 MB/sec
  Reflects heavy consumer fan-out
BSP v2.0:
  OMB focused primarily on producer throughput and latency
  Direct BytesOut comparison requires real workload metrics
Assessment:
  BSP v1.0 demonstrates strong consumer-side throughput
  BSP v2.0 expected to match/exceed under production load

## Slide 8: Replication Traffic Behaviour
BSP v1.0:
  Replication BytesIn: 60–200 MB/sec
  Periodic spikes up to ~400 MB/sec
  Healthy replication with no persistent backlog
BSP v2.0:
  Replication Factor = 4, min.insync.replicas = 3
  Replication overhead higher but within expected bounds
  No replication throttling or instability observed
Assessment:
  Both platforms exhibit expected HA replication behaviour

## Slide 9: Reassignment & Operational Stability
BSP v1.0:
  Partition reassignment traffic near zero
  Indicates stable, balanced cluster
BSP v2.0:
  No reassignment activity during benchmarks
  KRaft controllers remained stable under load
Assessment:
  Operational stability comparable between platforms
  KRaft control plane behaves predictably

## Slide 10: Latency Characteristics
BSP v1.0:
  Latency not explicitly isolated in Grafana views
  Production workloads trade throughput for acceptable latency
BSP v2.0:
  OMB provides detailed latency metrics
  P50 latency low under moderate load
  P99 / P99.9 increase under saturation
  Tail latency influenced by shared infra and disk contention
Assessment:
  Latency acceptable for enterprise Kafka workloads
  Expected to improve with dedicated resources

## Slide 11: Architectural Comparison
BSP v1.0: VM-based, ZooKeeper, vertical/manual scaling
BSP v2.0: Containerised, KRaft, horizontal declarative scaling
BSP v2.0 enables:
  Native Kubernetes automation
  Improved isolation at pod level
  Rolling, declarative upgrades
  Enhanced observability (Grafana + K8s metrics)

## Slide 12: Limitations of Current Comparison
BSP v2.0 tests were time-bound (~5 minutes)
Executed on shared BCP v2 infrastructure
No long-running production-equivalent workloads yet
BytesOut and replication under real traffic pending

## Slide 13: Final Conclusion
BSP v2.0 on BCP v2 is technically capable of matching or exceeding BSP v1.0 throughput
No structural performance regression observed moving to OpenShift + CFK
Primary difference today is operational maturity, not capability
With dedicated worker nodes and sustained workloads, BSP v2.0 is expected to:
  Meet or exceed BSP v1.0 performance
  Deliver superior scalability, resilience, and operational efficiency